## Slide 1: Optimal Energy Management of Renewable Energy Communities: a Multi-Agent Reinforcement Learning Approach
Samuele Delpero Davide Salaorni Marcello Restelli
samuele.delpero@mail.polimi.it davide.salaorni@polimi.it restelli.marcello@polimi.it

## Slide 2: RECs – An overview
Groups of buildings that share renewable energy
Approved at the EU level in 2018 [1] Aims at climate neutrality by 2050
Goal: increasing the self-consumption
[1] Directive (EU) 2018/2001 of the European Parliament and of the Council of 11 December 2018 on the promotion of the use of energy from renewable sources. https://eur-lex.europa.eu/eli/dir/2018/2001/oj/eng

## Slide 3: RECs – Structure
Nodes can be pure consumers, producers or prosumers
Private households, public facilities and commercial buildings
No change in grid architecture
No change in contracts with energy providers

## Slide 4: RECs – Objectives
Clean energy
Decrease in fossil fuels
Environmental benefits
Less energy transport
Lower peaks
Infrastructural benefits
Economical benefits
Sustainability awareness
Energy democracy
Social benefits

## Slide 5: Control problem
Plan:
Battery usage
Incentive distribution
Controllers:
Batteries
REC

## Slide 6: Related works
[1] Pasqui, Mattia, Alex Felice, Maarten Messagie, et al. “A New Smart Batteries Management for Renewable Energy Communities.” Sustainable Energy, Grids and Networks 34 (June 2023): 101043. https://doi.org/10.1016/j.segan.2023.101043.
[2] Palma, Giulia, Leonardo Guiducci, Marta Stentati, Antonio Rizzo, and Simone Paoletti. “Reinforcement Learning for Energy Community Management: A European-Scale Study.” Energies 17, no. 5 (2024): 5. https://doi.org/10.3390/en17051249.
Pasqui et al. [1]:
  Battery control: rule-based
  Incentive distribution: rule-based
  Limits: rule-based policies lack flexibility
Palma et al. [2]:
  Battery control: central RL agent
  Incentive distribution: not considered
  Limits: totally collaborative

## Slide 7: Node agent
Objectives:
Minimize:
  energy purchase cost
  battery degradation
Maximize:
  energy sale revenue
  REC incentives
Decision making: battery charge and discharge

## Slide 8: REC agent
Objective: maximize self-consumption
Decision making: distribution of incentives to nodes

## Slide 9: Agents’ interaction

## Slide 10: INAIA algorithm
The REC agent simulates the node agents
Responsiveness to incentives is considered
Batteries modelled with Digital Twin
Salaorni, Davide, Federico Bianchi, Silvia Colnago, Andrea Barisione, Francesco Trovò, and Marcello Restelli. “A Novel Digital Twin for Battery Energy Storage Systems in Micro-Grids.” Journal of Energy Storage 132 (October 2025): 117745. https://doi.org/10.1016/j.est.2025.117745.

## Slide 11: Datasets
397 year-long profiles from [1]
Demand
Realistic synthetic data from PVGIS [2]
Generation
Hourly prices from the Italian energy market [3]
Market
Daily temperature from [4]
Temperature
[1] Fioriti, Davide, Luigi Pellegrino, Giovanni Lutzemberger, Enrica Micolano, and Davide Poli. “Optimal Sizing of Residential Battery Systems with Multi-Year Dynamics and a Novel Rainflow-Based Model of Storage Degradation: An Extensive Italian Case Study.” Electric Power Systems Research 203 (February 2022): 107675. https://doi.org/10.1016/j.epsr.2021.107675.
[2] Photovoltaic Geographical Information System tool. https://re.jrc.ec.europa.eu/pvg_tools/en/
[3] Gestore Mercati Energetici. https://www.mercatoelettrico.org/it/download/DatiStorici.aspx
[4] Staffell, Iain, Stefan Pfenninger, and Nathan Johnson. “A Global Model of Hourly Space Heating and Cooling Demand at Multiple Spatial Scales.” Nature Energy 8, no. 12 (2023): 1328–44. https://doi.org/10.1038/s41560-023-01341-5.

## Slide 12: Baselines
Rule-based: the REC agent rewards the households proportionally to their contribution to the current self-consumption
PPO [1]: the REC agent is trained with Proximal Policy Optimization
LOLA [2]: the REC agent is trained with the LOLA algorithm
[1] Schulman, John, Filip Wolski, Prafulla Dhariwal, Alec Radford, and Oleg Klimov. “Proximal Policy Optimization Algorithms.” arXiv:1707.06347. Preprint, arXiv, August 28, 2017. https://doi.org/10.48550/arXiv.1707.06347.
[2] Foerster, Jakob N., Richard Y. Chen, Maruan Al-Shedivat, Shimon Whiteson, Pieter Abbeel, and Igor Mordatch. “Learning with Opponent-Learning Awareness.” arXiv:1709.04326. Preprint, arXiv, September 19, 2018. https://doi.org/10.48550/arXiv.1709.04326.
Metrics
Local reward: the reward of the node agents not including the REC incentives
Total reward: the reward of the node agents including the REC incentives
Social welfare: sum of the total reward for all node agents
Self-consumption:

## Slide 13: Scenario 1: performance and scalability
The performance of INAIA gets better as the number of agents increases
Algorithm | Social Welfare [€] |  |  | Self-Consumption [MWh] |  | 
 | 3 | 5 | 8 | 3 | 5 | 8
Rule-based | -2651 | -4016 | -4908 | 3.67 | 8.81 | 11.66
PPO | -2673 | -4104 | -5125 | 3.46 | 7.82 | 10.69
LOLA | -2875 | -4637 | — | 3.28 | 5.90 | —
INAIA | -2579 | -3780 | -4264 | 4.68 | 16.65 | 85.74
% vs. RB | -2.72% | -5.88% | -13.12% | 27.5% | 89.0% | 735%
Cumulative metrics over 5 years

## Slide 14: Scenario 2: why join a REC?
Households with solar panels in different orientations
17.3 % more self-consumption w.r.t. the best baseline

## Slide 15: Conclusions
More clean energy
Less strain on the grid
Increase in self-consumption
Economic benefits
Energy democracy
Incentives to members
Fairness among members
Future work

## Slide 16: Thanks for your attention
INAIA-REC
check out the repository

## Slide 17
samuele.delpero@mail.polimi.it
www.polimi.it

## Slide 18: RECs – Incentives
Refund for spared infrastructure maintenance due to self-consumption
Amounts to 8–10 €/MWh
Main incentive component
Amounts to 80–120 €/MWh
Depends on market price
Compensation for self-consumed energy
Incentive tariff

## Slide 19: MDP details
Observations:
Local data
  Energy demand and production
  Battery level and temperature
  Energy prices
Global data:
  Aggregates of withdrawal and injection
Time
Actions: current to apply to the battery
Reward:
Trading: from exchanges with the grid
Degradation: from battery usage
Incentives: issued by the REC
Observations:
Local data:
  Demands and productions
  Battery usage
Global data:
  Aggregates of demand, production and battery usage
  Aggregates of withdrawal and injection
Time
Actions: distribution of the incentives
Reward: REC self-consumption
Node agent
REC agent

## Slide 20: INAIA algorithm

## Slide 21: Node agent – network policy
ι: mean current to battery
During training action sampled from normal distribution with mean ι

## Slide 22: REC agent – network policy
Multi-branch network
One branch per node agent

## Slide 23: REC agent – network policy
During training action sampled from Dirichlet distribution with parameters Softplus(p)

## Slide 24: RECs – Objectives
Environmental benefits
Infrastructural benefits
Social benefits

## Slide 25: RECs – Objectives
Clean energy production
Decrease usage of fossil fuels
Meet EU climate neutrality targets
Environmental benefits
Decrease in transport of energy
Lower peaks
Less energy loss
Infrastructural benefits
Economical benefits to families
Increase in sustainability awareness
Energy democracy
Social benefits

## Slide 26: Agents’ interaction
The node agents share local data
The REC agent shares aggregates of local data and incentives